## Slide 1: The Variables of a Trebuchet!
Some Simple
Some Complex

## Slide 2: Amount of Weight
More Weight
  Flies Farther
  Swings Arm Faster
  Could change the release point and cause it the fly higher than before
Less Weight
  Just the opposite!

## Slide 3: Arm: Length and Pivot Point
Longer Arm
  Adds Range
  Takes Longer to Rotate
Pivot Point
  Changes Ratio that Force is Applied
  1:5 Ratio is a Good Starting Point
  Too Much Ratio Can Decrease Efficiency

## Slide 4: Release Pin
More Upright
  Releases Later in the Throw
  Lower Trajectory
More Bent Back
  Releases Earlier in the Throw
  Higher Trajectory
  Could Fire Backwards!
Lighter Projectile – More Bent Back
Heavier Projectile – More Upright

## Slide 5: Sling Length
Short
  Releases Projectile Sooner
  Swings Faster
Long
  Releases Projectile Later in the Cycle
  Swings Slower
The Sling should be In-Line with the Arm when the Weight is at Minimum Potential Energy

## Slide 6: Counterweight Position
Design Types Listed in Order of Efficiency:
  Floating Axel Counterweight (FA)
    Weight Falls Strait Down
  Offset Counter Weight (OCW)
    Weight Falls in an Arc and Strait Down Pattern
    More Offset, the Better
  Fixed Counter Weight (FCW)
    Weight Falls in an Arc Pattern
The Straighter the Counterweight Falls Down, the More Efficient it Will Be!

## Slide 7: So, What Do I Change?
Listed in order of impact and ease of change:
  Release Pin
  Weight
  Sling Length
  Counterweight Position
  Arm Length and Pivot Point

## Slide 8: Summary of Changes
Lower Trajectory
  Release Pin More Upright
  Shorter Sling Length
Higher Trajectory
  Release Pin More Bent Back
  Longer Sling Length
Weight, Arm Length and Pivot Point, Counterweight Position
These Can Also Change Trajectory But is Highly Dependant on Where the Current Timing of the Cycle is.
  More Weight Can Throw off the Timing and Be Less Efficient.
  More Arm Length Without More Weight can reduce range.